## Slide 1: WHMIS
What students need to know

## Slide 2: WHMIS Stands for…
Workplace
Hazardous
Materials
Information
System

## Slide 3: What does it do?
4 Main Parts of WHMIS
  Classification and symbols for hazardous materials
  Labels
  Material Safety Data Sheets (MSDS)
  Worker Education

## Slide 4: Canadian Standard
All schools and workplaces in Canada use this hazard labeling system
All students and workers in Canada must be WHMIS trained

## Slide 6: Why is it so Important?
Notes: Discuss with class

## Slide 7: Safety First
Everyone has a RIGHT TO KNOW about health and safety hazards
WHMIS labeling helps stop injuries, illness, deaths, medical costs, fires, and explosions caused by UNSAFE use of hazardous chemicals

## Slide 8: In other words…
TO PROTECT YOU!!!!

## Slide 9: The 6 Classes
All WHMIS controlled products fall into one or more of 6 classes of hazardous materials
Class A: Compressed Gas
Class B: Flammable and Combustible Material
Class C: Oxidizing Material
Class D: Poisonous and Infections Material
    D1 – Materials causing immediate and serioius toxic effects
    D2 – Materials causing other toxic effect
    D3 – Biohazardous Infectious Materials
Class E: Corrosive Material
Class F: Dangerously Reactive Material

## Slide 10: Meet the Symbols

## Slide 11: Class A: Compressed Gas
RISKS:
  compress gas canisters may explode due to high pressure
EXAMPLES:
  oxygen, acetylene, propane, some aerosols

## Slide 12: Class B: Flammable
RISKS:
  may burn and cause fire
EXAMPLES:
  gasoline, chlorine

## Slide 13: Class C: Oxidizing Material
RISKS:
  may help other materials burn
EXAMPLES:
  potassium chloride, nitric acid, ozone

## Slide 14: Class D-1: Toxic (immediate)
RISKS:
  chemical causing immediate serious illness
EXAMPLES:
  cyanide, carbon monoxide

## Slide 15: Class D-2: Toxic (long term)
RISKS:
  chemical causing other toxic effects (eg. eye/skin irritation, cancer)
EXAMPLES:
  mercury, lead, arsenic

## Slide 16: Class D-3: Biohazardous
RISKS:
  infectious materials causing illness or disease
EXAMPLES:
  bacteria (E.coli), virus (HIV)

## Slide 17: Class E: Corrosive
RISKS:
  Causes burns to skin, eyes, lungs, clothes and metals
EXAMPLES:
  hydrochloric acid, sodium hydroxide

## Slide 18: Class F: Dangerously Reactive
RISKS:
  Causes burns or explode if heated, shaken or mixed
EXAMPLES:
  nitroglycerine, aluminum chloride

## Slide 19: WHMIS Labels
  All WHMIS controlled chemicals must be labeled
  To identify a WHMIS label, look for the cross hatched border on the chemical container

## Slide 20: WHMIS Labels
Supplier Label
Workplace Label

## Slide 21: WHMIS Labels
  Supplier labels are provided by the manufacturer of the chemical and must include:
    Name of product
    Supplier identifier
    Statement referring to MSDS
    Hazard symbols
    Risk phrases
    Precautionary measures
    First aid treatment

## Slide 22
How do you know that this is a WHMIS label by looking at it?
Answer:
It has a hatched border

## Slide 23
Name the hazard categories that acetone belongs to:
Answer:
Class B: Flammable
Class D3: Toxic (long term)

## Slide 24
What safety equipment should you wear when handling acetone?
Answer:
Goggles and Gloves

## Slide 25
What should you do if you get acetone on your skin?
Answer:
Wash with soap and water

## Slide 26
Who is the supplier of this acetone product?
Answer:
BIG Chemical Company

## Slide 27
What’s that?

## Slide 28: MSDS Stands for…
Material
Safety
Data
Sheet

## Slide 29: MSDS
    Product identification and uses of the product
    Hazardous ingredients
    Physical data
    Fire and explosion data
    Reactivity data
    Toxicological properties
    Preventive measures
    First Aid Measures
    Source of MSDS and data
  Contains detailed information about a WHMIS controlled product including:

## Slide 30: MSDS example

## Slide 31: MSDS practice
What is the full name of the product?
  Hydrochloric Acid Solution, 0.1M
  Section 1
Name the manufacturer, their location and emergency contact information.
  Columbus Chemical Industries
  Columbus, WI.
  CANUTEC (Canada): 613-424-6666
  Section 1

## Slide 32: MSDS practice
What safety equipment should you wear when handling this product
  Goggles, gloves and apron
  Section 8
What should you do if you get this product on your skin?
  Flush with water for 15 minutes
  Section 4

## Slide 33: MSDS practice
What should you do if you swallow this product?
  Call Poison Control immediately. Do not induce vomiting. Rinse mouth with cold water. Drink 1-2 cups of water.
  Section 4
Does this product have an odor?
  Yes
  Section 2

## Slide 34: MSDS practice
What is the WHMIS classification of this product?
  Class E: Corrosive liquid
  Section 15
What percentage of the solution is water?
  98-99%
  Section 3

## Slide 35: Does EVERYTHING get a WHMIS label?
What do you think? (brainstorm in small groups)
Answer:
NO!!!

## Slide 36: Does EVERYTHING get a WHMIS label?
Materials must be HAZARDOUS and be used in the WORKPLACE to be WHMIS controlled!

## Slide 37: Hazardous Household Product Symbols

## Slide 38: Hazardous Household Product Symbols (HHPS)
You will find other symbols on products purchased commercially for home use
  Eg. hairspray, garden herbicides, cleaners
For your safety, you should be able to recognize these symbols and understand what hazards they represent

## Slide 39: Hazardous Household Product Symbols (HHPS)

## Slide 40
Poisonous
  May be lethal or cause serious irreversible effects
Flammable
  May ignite if exposed to a spark or flame or spontaneously
Explosive
  Under pressure and may explode if heated
Corrosive
  Will cause chemical burns

## Slide 41: Now that you know…