Resistance

- Electrons do not move through all materials equally well

- Some materials resist the flow of charge and use the energy from the electrons as the current tries to move through

Applications of Resistors:

Resistors have many important uses, including

- Converting electrical energy to heat & light

- Controlling current and voltage through a circuit

Factors Affecting Resistance

The resistance of a material depends on:

- The type of the material → the poorer the conductor, the greater the resistance

- The thickness of the wire → the thinner the wire, the greater the resistance

- The length of the wire → the longer the wire, the greater the resistance

- The temperature of the wire → the higher the temperature, the greater the resistance

- Resistance is defined as the ratio of the potential difference across a load (how much energy is lost) to the current through the load

|  | Symbol | Unit |
| --- | --- | --- |
| Resistance | R | Ohms (Ω) |
| Voltage | V | Volt (V) |
| Current | I | Ampere (A) |

This equation is referred to as Ohm’s Law after the scientist who discovered it.

## Sample Problem

What is the resistance of the heating coil of an electric heater, if a current of 12.5 A runs through it when it is connected to a 120 V wall outlet?

Solution

| G iven | V = 120 V I = 12.5 A |
| --- | --- |
| R equired | R = ? |
| A nalysis |  |
| S olution |  |
| S tatement | The resistance of the electric heater is 9.60 Ω. |

Classwork/Homework

- Complete Resistance problems (#3 a-f) of Electricity Problem Sets handout on a separate sheet of paper.

Use GRASS and show all of work.